## Slide 1: Lightweight Approximate Multiplier with Improved Accuracy in FPGA for Error Resilient Application
Mr. Apurba Prasad Padhy, Dr. Bishnu Prasad Das
https://ieeexplore.ieee.org/document/10089951
Presented By: Akarshi Roy Choudhury

## Slide 2: APPROXIMATE COMPUTING
Achieve high performance and efficiency
Used in error resilient operations like signal processing, image processing
Multiplication - a fundamental operation in such applications

## Slide 3: LACUNAE AND PROBABLE SOLUTION
Machine learning and image processing applications work on large-scale multiplication.
DSP(digital signal processing) blocks in FPGA are employed for fast multiplication.
The DSP-based multipliers are unable to provide such high speed and latency. Thus, they can’t provide as much efficiency as expected.
SOLUTION
APPROXIMATE MULTIPLIER

## Slide 4: APPROXIMATE MULTIPLIER
For applications requiring fast multiplication, high performance and area efficient approximate multipliers can be used, instead of accurate multipliers.
FPGA-based 4x4 approximate multiplier using 12 LUTs and one carry chain, has been proposed earlier.
However, there are many error cases, which lead to a significant decrease in accuracy in the subsequent higher order multipliers designs

## Slide 5: IMPROVED PROPOSITIONS
1.) The proposed 4x4 approximate multiplier has been optimised for the 6-input LUTs, available in modern FPGAs.
2.) The partial product matrix is divided into two parts and the computation is approximated, resulting in requirement of only 11 LUTs.
3.) The 4x4 multiplier is scalable to higher order multipliers. Three methods of implementation of 8x8 multipliers from 4x4 multipliers have been proposed, and their power, area and latency have been compared.
4.) Further, the 8x8 multiplier has been employed in image sharpening applications.

## Slide 6: DESIGN OF 4X4 APPROXIMATE MULITPLIER
Consider two 4-bit numbers: A(A3A2A1A0) and B(B3B2B1B0)
The partial product matrix is as follows:
Four partial products, each of length 4-bit, are produced.
Fig.1 Partial product matrix of 4 × 4 multiplication

## Slide 7: DIVISION OF PARTIAL PRODUCT MATRIX
The partial products matrix is divided into two parts, namely Part I and Part II, as shown below.
Fig.2 Part I and Part II of the partial product matrix

## Slide 8: ANALYSIS OF PART I
The input variables in Part I are A0, B0, A1, B1, A2 and B2.
The corresponding six terms are used to generate the intermediate sum [T2G2P2P1P0], as shown in Fig.2(a).
Thus, Part I requires 3 LUTs.
P0,P1 (4 shared variables): 1 LUT
P2 (6 variables): 1 LUT
G2 (6 variables): 1 LUT
T2 (6 variables): 1 LUT => can be truncated

## Slide 9: ANALYSIS OF PART II
The input variables in Part II are A1, B1, A2, B2, A3 and B3 for the outputs [px4px3px2px1px0] and A0, A3, B0, B1 and B3 for the outputs [py2py1py0].
Thus, Part II requires 5 LUTs.
py1,py2 (5 shared variables): 1 LUT
px0,px1 (5 shared variables): 1 LUT
px2 (6 variables): 1 LUT
px3 (6 variables): 1 LUT
px3 (6 variables): 1 LUT

## Slide 10: ANALYSIS OF FINAL STAGE
The proposed design uses 8-bit binary adder, instead of 8-bit ternary adder, thereby decreasing latency by 37%.
Thus, the final stage is implemented using 3 LUTs and a carry chain as binary adder with G2 as Cin.
Fig.3 LUT-based implementation of Part I and Part II for proposed 4×4 approximate multiplier
Fig.5 Final Stage architecture of proposed approximate multiplier
Fig.4 Final Stage representation

## Slide 11: APPROXIMATION
Removal of T2 in the final stage calculation improves speed of the design by eliminating 1 LUT. Therefore, 11 LUTs are required for implementing the proposed 4x4 approximate multiplier.
However, when A0, B0, A1, B1, A2 and B2 all are fed logic 1 simultaneously, the output obtained is 10001. Since T2 had been truncated, hence an error of magnitude 16(10001-0001) is generated as a 5-bit output(T2G2P2P1P0) can’t be represented accurately by a 4-bit output(G2P2P1P0).
To mitigate this problem, values of G2 and P2 have been reassigned as 1, instead of 0, when T2 is 1, thus, minimising the error.

## Slide 12: MODIFICATION IN EXPRESSION OF P2 AND G2
The Boolean expressions of P2 and G2 have been modified as follows:
The error magnitude gets reduced from 16 to 4(10001-1101).
This completes the entire design for the 4x4 approximate multiplier. On testing against all the 16x16=256 cases, error of magnitude 4 was found only in 4 cases, as shown in table I.

## Slide 13: DESIGN OF HIGHER ORDER APPROXIMATE MULTIPLIER
Modular approach has been used to design higher order approximate multipliers.
This paper has discussed the design of 8x8 approximate multipliers, followed by their error analysis and implementation of image sharpening application.
Three approaches have been proposed for the design of 8x8 approximate multipliers, using the proposed 4x4 approximate multiplier.

## Slide 14: APPROACH 1
4 instances of the proposed 4x4 approximate multiplier
2 instances of accurate 4-bit tertiary adder
Utilises 53 LUTs
Better performance than Ca [1], which uses 57 LUTs (4 instances of 4x4 multiplier proposed in [1] and accurate ternary adder)

## Slide 15: APPROACH 2
Novel approximate adder has been used, to add the output of sub-multipliers.
The approximate adder, implemented using OR gates, adds the terms of same bit location into a 1-bit result without considering the carry-out from the previous bit location.
4 instances of proposed 4x4 approximate multiplier (11x4=44LUTs)
8 instances of novel approximate adder (1x8=8LUTs)
Utilises 52 LUTs
Better performance in comparison to Cc [1], which utilises 56 LUTs

## Slide 16: APPROACH 3
Fig.5 8 × 8 approximate multiplier with estimated addition of sub-products.
Approach 3(a): Utilises 45 LUTs
Approach 3(b): Utilises 44 LUTs
Most area-efficient approximate multiplier

## Slide 17: ERROR ANALYSIS
Error analysis has been performed on the proposed 4x4 and 8x8 approximate multipliers based on following parameters.
Average Relative Error (ARE):
Average Error (AE):
Error Occurrences: Total number of inaccurate test cases
Maximum Error Magnitude: Maximum magnitude of error among all the error occurrences
Maximum Error Occurrences: Number of times the maximum error magnitude occurs

## Slide 18: ERROR ANALYSIS OF PROPOSED 4X4 APPROXIMATE MULTIPLIER
Table II shows the error analysis of the proposed 4x4 approximate multiplier, in comparison with 4x4_approx[1].
TABLE II

## Slide 19: ERROR ANALYSIS OF APPROXIMATE 8X8 MULTIPLIERS
Table III shows the error analysis of the proposed three approaches of the 8x8 approximate multipliers.
TABLE III

## Slide 20: PERFORMANCE ANALYSIS
Performance analysis has been performed on the proposed 4x4 and 8x8 approximate multipliers based on performance parameters such as:
LUT utilisation
Power
Latency

## Slide 21: PERFORMANCE ANALYSIS OF 4X4 APPROXIMATE MULTIPLIER
Table IV shows the performance analysis of the proposed 4x4 approximate multiplier, in comparison with 4x4_approx[1].
The proposed 4x4 approximate multiplier has 26.7% LUT saving, 57.6% power saving and 60.1% latency improvement in comparison to Xilinx multiplier IP.
TABLE IV

## Slide 22: PERFORMANCE ANALYSIS OF 8X8 APPROXIMATE MULTIPLIERS
Table V shows the performance analysis of the proposed 4x4 approximate multipliers.
TABLE V

## Slide 23: IMAGE SHARPENING ANALYSIS
To further evaluate the quality of the proposed 8x8 multipliers, image sharpening application has been implemented. The PSNR(peak signal to noise ratio) has been evaluated and compared. The results are shown in table VI. value are shown in table VI.
The PSNR values of the proposed approximate multipliers are well within the acceptable range. Higher the PSNR, better the image quality.
TABLE VI

## Slide 24: CONCLUSION
A 4x4 approximate multiplier has been proposed, which utilises 11 LUTs.
Higher order multipliers (8x8) have been implemented using the proposed 4x4 approximate multiplier.
Error analysis showed that the proposed approximate multipliers are successful in reducing the error magnitude.
Performance analysis showed that the proposed approximate multiplier out performed the state-of-the-art multipliers, in terms of LUT utilisation, power and latency.
The computation of PSNR values validated that the proposed approximate multipliers can be used for error-resilient applications.

## Slide 25: REFERENCE
[1] https://ieeexplore.ieee.org/abstract/document/9344673